## Slide 1: RHPWG – Control Measures Subcommittee Oil & Gas Source Coordination
WRAP- Oil and Gas Workgroup Bi-monthly Call
June 11, 2019

## Slide 2: Control Measures Subcommittee - Background
Membership
  AZ, Albuquerque, CA, CO, ID, MT, NV, NM, WA, WY and FLMs
Task 5.1: Develop criteria for source identification and 4-factor analysis (completed)
  “Reasonable Progress Source Identification and Analysis Protocol” document is completed and posted on the CM Subcommittee webpage
    Provides a framework for identifying and screening emission sources potentially impacting Class I area visibility
    Methodology loosely based on past EPA approved RH SIPs and draft EPA guidance
      Uses 2014 NEI
      Focus on point source emissions of NOx, SO2, and PM10
    Protocol document does not limit in any way the ability of a state from pursuing alternative approaches or methods for identifying and evaluating emission sources
    Encourages consistency among WRAP states in identifying sources subject to a four-factor analysis evaluation

## Slide 3: Control Measures Subcommittee - Background
Task 5.3: Conduct regional/state source screening (completed)
  WRAP contracted with Ramboll to develop a Q/d analysis for the Class I areas in the 15 western states
    Completed Q/d analysis is available in both spreadsheet and database formats available at:
      http://views.cira.colostate.edu/tssv2/Emissions/QDAnalysis.aspx
      Default setting identifies point sources with 2014 emissions over 25 tpy of NOx, SOx and PM10 with a Q/d > 10
    Subcommittee reviewed the analysis and provided feedback to Ramboll
    Analysis allows for transparency of sources impacting various Class I areas
Continued
Notes: Under Task 5.3 the Subcommittee asked for contractor support in screening sources.
Mention the Weighted Emissions Potential work

## Slide 4: Control Measures Subcommittee – Current Work
Workplan Tasks for the Next Several Months
  Identify 2028 control strategies and incorporate in 2028 inventory (in progress/ongoing)
      Some states working on control strategy analysis now
      Other states are in the process of notifying sources and starting the control strategy analysis work
        WRAP goal – states complete the four-factor control strategy analysis by late 2019
        Allows states to forecast emission reductions from anticipated controls into 2028 Reasonable Progress modeling analysis
      Draft Source Control Assessment Considerations memo
        Assist states in performing the four-factor analysis

## Slide 5
WRAP States Status for Sources Identified as Subject to Reasonable Progress 4-Factor Analysis Process |  | 
Jurisdiction | Has notified sources? | Notes on methodology
Alaska | No | Tentatively, using Q/d>10 with Q>25 tpy. Tentatively identified 7 sources, including an airport and AFB
Albuquerque | Have begun discussion with the one RP source identified for Albuquerque-Bernalillo County. | Albuquerque working in concert with New Mexico for unified statewide analysis. See entry for New Mexico, below.
Arizona | Has held stakeholder meeting. | Currently using a Q/d of 20, about 15 identified sources. Have received feedback to lower Q/d to 10, which could bring in 3 additional sources. Those numbers exclude airports and rail yards.
California | Checking with local air quality management districts | May identify more than 100 sources, probably based on Q/d of 10.
Colorado | 22 sources identified, have been notified by letter. RH stakeholder meeting in June. | Using Q/d threshold of 10 based on Q over 25 tpy. Currently 22 sources identified.
Hawaii | 8 sources identified. | Using Q>25 tpy and Q/d threshold of 10. 8 sources identified, two airports screened out and sugar mill shutdown.
Idaho | Have not yet contacted facilities. | Used Q of 25, Q/d of 2. Initial list identified 12 sources. The list was reduced to three sources by excluding an airport and running a CALPUFF visibility impact analysis.
Montana | Have notified all screened sources by letter and phone call. | Q/d of four, looking at NOx and SO2 only. Identified 17 sources
Nevada | Checking – awaiting response | Q/d of five, which initially identified seven sources, one of which is an airport which will be excluded.
New Mexico | Have not begun notifying non-Albuquerque sources as of date of call, will be notifying them by letter soon. | Q/d of 10, resulting in 13 sources for New Mexico outside Albuquerque-Bernalillo County. One source was identified for Albq-BC. Thus, 14 sources statewide.
North Dakota | 10 sources notified by letter. | Using Q/d of ~10. PM10 excluded from Q.
Oregon |  | State contacted, awaiting response
Utah | Contacted 4 sources | Currently evaluating whether to use a Q/d that is less than 10.
South Dakota |  | State contacted, awaiting response
Washington | Goal to draft letters to local air quality agencies by the week of May 27th and letters to sources will go out the following week. | Q/d of 6.5, about 18 sources, excluding airport.
Wyoming | Have not begun notifying sources. | Still finalizing Q/d analysis.

## Slide 6: Oil & Gas Source Sector Evaluation
The WRAP Q/d analysis screening tool screening based on NOx, SO2 and PM10 emissions
  Oil & Gas VOC emissions are not significant contributors to regional haze
Using the WRAP Q/d analysis screening tool at a Q/d threshold of 10 shows AZ, ND, NM and WY have identified a few gas plants and compressor stations for potential 4-factor review
Some states evaluating whether to conduct 4-factor review on significant Oil & Gas area source categories
  May depend on the permitting threshold in each state and level of area source emissions