## Slide 1: Summary of Denver-Julesburg Basin Drill Rig 1-hr NO2 Impacts Study
Kickoff Meeting of Model
Evaluation Workgroup
John Bunyak, westar
August 14, 2015

## Slide 2: Site Location Selected for This Study: Northeast Colorado Near Platteville in Denver-Julesburg Basin (Site access provided by Anadarko Petroleum Corp.)

## Slide 3: Study Purpose
To collect emissions and ambient data near drill rigs to evaluate 1-hr NO2 impacts from drilling operations
To use the emissions and ambient data to evaluate AERMOD w.r.t. drilling operations

## Slide 4: Study Management
Study Management Team—Provide Direction and Guidance
  Mary Uhl—BLM
  Chris Owen—EPA
  Darla Potter—WDEQ
  Cathe Kalisz—API
  Doug Blewitt—Consultant to API
WESTAR—Provide Assistance to the Study Management Team
  Tom Moore—Program Director
  John Bunyak—Consultant to WESTAR—Project Manager
AECOM—Contractor that conducted the field study
Amec Foster Wheeler—Contractor that performed data analysis and formatting

## Slide 5: Denver-Julesburg Basin Field Study Approach
Continuously monitor NOx, NO, and NO2 emissions from the diesel engines that power a drilling rig
Continuously monitor CO2, O2, Temperature, and Pressure of the engine exhaust
Continuously monitor 1-hour average levels of NO and NO2 in the near-field ambient air at 12 sites upwind, downwind, and crosswind to the drilling rig
Continuously monitor levels of O3 in the ambient air at one upwind and downwind site
Continuously monitor wind speed and wind direction at one upwind and downwind site and on a 10-meter instrumented tower
Site 1 monitoring was conducted from October 10-26, 2014
Site 2 monitoring was conducted from November 3-16, 2014

## Slide 6: Monitor Deployment
Monitors were mounted on portable trailers to facilitate moving the monitors as needed throughout the study periods
AERMOD modeling was conducted to help with the initial monitor placement
AERMOD results showed that the peak modeled NOx concentrations were located inside the drill pad
For Site 1, the monitors were positioned near the pad boundary based on predominant winds, but were not relocated due to airflow obstructions, off-pad access limitations, and power constraints
For Site 2, the monitors were repositioned based on prevailing wind forecasts

## Slide 7: Site 1 Monitor Deployment
NO and NO2 were monitored at 12 sites along the well pad perimeter
  6 sites near the northwest corner of the well pad, oriented with respect to predominant daytime winds
  6 sites near the southeast corner, oriented with respect to predominant nighttime winds

## Slide 8: Site 1 Monitor Deployment

## Slide 9: Site 2 Initial Monitor Deployment

## Slide 10: Site 2 Final Monitor Deployment

## Slide 11: AECOM Deliverables
All five-minute and hourly CEM, ambient pollutant, and meteorological data for both drill pads
Plot plans, including detailed site layout of the NOx monitors and drill pad structures
Calibration records for ambient pollutant monitors
CEM operation logs for emission sources
Final Field Study Report and Quality Assurance Project Plan

## Slide 12: AMEC Tasks
Perform Data Quality Review
  Alaska data—cursory review
  Colorado data—detailed review
Prepare CO data for analyses
Perform Data Analyses on CO data
Format CO data for AERMOD model evaluation
Prepare Report of work completed

## Slide 13: Next Steps for Workgroup
Continue data analyses and formatting
Fill in data gaps (e.g., emissions, met., etc. (see agenda for discussion topics)
Develop a draft model evaluation protocol
Conduct Model Evaluation
Document results