## Slide 1: WRAP Regional Haze Modeling
2028 Visibility Projections and First Round of Potential Additional Controls (PAC1)
RTOWG Webinar
July 15, 2020

## Slide 2: Introduction
2028 Visibility Projections
  Two sets of 2028 visibility projections made so far using EPA default visibility projection approach and CAMx modeling results:
    RepBase/2028OTBa w/ RepBase fires
    2014v2/2028OTBb w/ 2014v2 actual fires
Developed two alternative 2028 visibility projection approaches:
  EPAwoF: Like EPA default using RRFs based on modeling results for days from 2014 IMPROVE MID only without using modeled contributions from fires that are eliminated using source apportionment
  ModMID: Use modeled most U.S. anthropogenic emissions impaired days from 2014 IMPROVE sample days with contributions of fires eliminated using source apportionment
MELA1
MEVE1
GUMO1

## Slide 3: EPA Default Future Year Visibility Projection Method
EPA recommended visibility projection method using RepBase and 2028OTBa CAMx modeling results that used 2014 base year meteorology but 2014-2018 base year emissions:
  Species-specific RRF based on ratio of 2028OTBa to RepBase CAMx modeling results averaged across observed IMPROVE 2014 MID
    RRF = ∑ CAMx 2014 MID2028 / ∑ CAMx 2014 MIDRepBase
  Apply RRF to IMPROVE 2014-2018 MIFD to obtained 2028 visibility projection
    Visibility MID20208 = IMPROVE MID2014-2018 x RRF
  Issue: Modeled fire impacts on IMPROVE 2014 MID can make RRF stiff and unresponsive

## Slide 4: Alternative 2028 Visibility Projection Approaches
Alternative 2028 projection methods to EPA default approach (EPAwoF and ModMID) do not produce very different visibility projections.
Largest differences with EPA default is for ModMID approach as it not only eliminates fire contributions in the RRFs but also using different days.
One reason alternative approaches don’t make huge differences is biggest impact of fires is on Organic Matter Carbon (OMC) whose RRF is already very stiff (close to 1.0) even without fires.
Example for BextOMC below for Yellowstone and RepBase source apportionment across 2014 IMPROVE MID
YELL BextOMC Extinction
SOAB
Wildfire

## Slide 5: Potential Additional Controls
Some WRAP states provided a first round of Potential Additional Controls (PAC1) in 2028 that are used to make 2028 PAC1 visibility projections
  Initial 2028 PAC1 visibility projections were made using EPA default projection approach
Issues found in 2028 emission inventories with double counted O&G sources mainly in New Mexico so doing minimal analysis of PAC1 results while fixing inventory
Expected state emissions reductions
  Actual emission reductions were different for some states

## Slide 6: Actual PAC1 Total Emission Reductions by State
 | NOx | SO2 | PM25 | Comment
AZ | 1,651 | 2,092 | -61 | Primarily EGUs + PM2.5 from fugitive dust
CO | 314 | 0 | -1 | O&G Non-Point
ID | 675 | 1,335 | -65 | Non-EGU Point
MT | 55 | 458 | 1 | O&G Point
ND | 4,118 | 18,655 | 0 | EGU Point
NM | 28,937 | 7,704 | 6 | O&G Non-Point and Point
NV | 1,006 | 885 | 126 | Mainly EGU, some Non-EGU
OR | 2,832 | 440 | 1,101 | Non-EGU Point
SD | 1 | 0 | 0 | 
UT | -1 | 0 | 0 | 
WA | 0 | 0 | 0 | 
WY | -2,272 | 3,467 | 1,406 | EGU and Non-EGU
AZ Fugitive Dust

## Slide 7: -0.2%
EGU and Non-EGU Point Sources
-0.2%
-2,000
-0.2%
-0.5%
-0.3%
-0.2%
-0.1%
-1.4%
-0.5%
-0.3%
-0.3%
-0.6%
-0.6%
-0.7%
-1,000
-2,000
-4,000
-18,000
-400
-600
-800
+4,000
+2,000
-700
-1,300
-400
-200
-400
-50
-2,800
-400
-4,500
Changes (TPY)
Percent Change in 2028 Visibility
(lower deciview value, better projected visibility in 2028)

## Slide 8
Oil and Gas and Fugitive Dust PM2.5
-25,000
-25,000
-3,000
-500
-700
Changes (TPY)
Percent Change in 2028 Visibility
(lower deciview value, better projected visibility in 2028)
-0.6%
-0.3%
-0.8%
-0.6%
-0.2%
-0.3%

## Slide 9: 2028 OTBa vs PAC1 MID Projections
Very small reductions in 2028 projected visibility due to PAC1 controls
  Max = -1.4% (-0.14 dv) @ SAGU, AZ
    2nd High = -1.1% (-0.16 dv) @ SACR, NM
  Mostly hundredths of dv
  73% of sites reductions of at least -0.01 dv
    Sites with no change away from emission reductions (e.g., CA)
 |  | 2028 (dv) |  | Difference | 
Site | State | OTBa | PAC1 | (%) | (dv)
SAGU1 | AZ | 10.13 | 9.99 | -1.4% | -0.14
SACR1 | NM | 14.71 | 14.55 | -1.1% | -0.16
BADL1 | SD | 11.84 | 11.74 | -0.9% | -0.10
SAPE1 | NM | 5.91 | 5.86 | -0.8% | -0.05
MEVE1 | CO | 6.19 | 6.15 | -0.8% | -0.05
WHPE1 | NM | 5.55 | 5.50 | -0.8% | -0.04
WHRI1 | CO | 4.48 | 4.44 | -0.7% | -0.03
LOST1 | ND | 16.25 | 16.14 | -0.7% | -0.11
WHIT1 | NM | 9.73 | 9.67 | -0.6% | -0.06
PEFO1 | AZ | 7.44 | 7.39 | -0.6% | -0.05
MOZI1 | CO | 4.88 | 4.85 | -0.6% | -0.03
BAND1 | NM | 8.02 | 7.97 | -0.6% | -0.05
WEMI1 | CO | 6.08 | 6.05 | -0.6% | -0.04
MOHO1 | OR | 8.35 | 8.30 | -0.6% | -0.05
THRO1 | ND | 13.95 | 13.86 | -0.6% | -0.08
BRID1 | WY | 6.33 | 6.29 | -0.6% | -0.04
TONT1 | AZ | 9.64 | 9.58 | -0.6% | -0.05
HECA1 | OR | 11.52 | 11.46 | -0.5% | -0.06
GRSA1 | CO | 7.54 | 7.50 | -0.5% | -0.04
CHIR1 | AZ | 8.73 | 8.69 | -0.5% | -0.04
GICL1 | NM | 7.18 | 7.15 | -0.5% | -0.03
SYCA2 | AZ | 10.99 | 10.94 | -0.5% | -0.05
GRCA2 | AZ | 6.37 | 6.34 | -0.4% | -0.03
BALD1 | AZ | 6.67 | 6.64 | -0.4% | -0.03
IKBA1 | AZ | 8.61 | 8.58 | -0.4% | -0.04
BOAP1 | NM | 10.04 | 10.00 | -0.4% | -0.04
CANY1 | UT | 6.15 | 6.12 | -0.4% | -0.02
MELA1 | MT | 15.44 | 15.38 | -0.3% | -0.05
CRMO1 | ID | 7.51 | 7.49 | -0.3% | -0.02
WICA1 | SD | 9.89 | 9.86 | -0.3% | -0.03
ROMO1 | CO | 7.46 | 7.44 | -0.3% | -0.02
THSI1 | OR | 10.78 | 10.75 | -0.3% | -0.03
SIAN1 | AZ | 8.50 | 8.48 | -0.3% | -0.02
BRCA1 | UT | 6.02 | 6.01 | -0.3% | -0.02
STAR1 | OR | 10.20 | 10.17 | -0.2% | -0.02
YELL2 | WY | 7.05 | 7.03 | -0.2% | -0.02
JARB1 | NV | 7.77 | 7.75 | -0.2% | -0.02
CAPI1 | UT | 6.67 | 6.65 | -0.2% | -0.02
VOYA2 | MN | 13.37 | 13.34 | -0.2% | -0.03
GUMO1 | TX | 12.27 | 12.24 | -0.2% | -0.03
KALM1 | OR | 11.54 | 11.51 | -0.2% | -0.02

## Slide 10: Conclusions 2028 PAC1
As expected, very small changes in projected 2028 MID dv
  Mostly hundredths of dv changes
  Largest changes in or near states with emissions reductions (e.g., NM, AZ, ND)
  Smallest changes away from such states (e.g., CA)
Round 2 of Potential Additional Controls (PAC2)
  Need state emission changes to be tested by Sept. 10, 2020
Caveats:
  2028OTB emissions include double counted O&G sources
    In both 2028OTBa and 2028PAC1
    Does not affect the reductions in 2028 MID due to PAC1 controls
    Probably minimal affect on 2028 MID projections