## Slide 1
Western States Air Resources Council Western Regional Air Partnership
Fire and Smoke Workgroup
February 28, 2022
Wildland Fire Emission
Factor Development
Shawn Urbanski
USDA Forest Service, Rocky Mountain Research Station
Missoula Fire Science Laboratory

## Slide 2: Missoula Fire Sciences Laboratory
Established by US Forest Service 1960 to find scientific solutions:
Better managing the nation’s wildland resources
Improve forest fire prevention and suppression
Currently the Missoula Fire Lab is part of the US Forest Service Rocky Mountain Research Station

## Slide 3: Fire, Fuel, and Smoke Science Program
Focus Areas:
Physical fire processes
Fuel dynamics
Smoke emissions and dispersion
Fire ecology
Fire and fuel management strategies
Science delivery
Headquartered at the Missoula Fire Sciences Laboratory
One of Seven Science Programs in the Rocky Mountain Research Station

## Slide 4: Societal Impacts Driving Smoke Research
Safety
Public Health
Scenic Integrity
Regulatory
Nuisance
Climate
Smoke is a major source of air pollution
Fine particulate matter (PM2.5) is primary pollutant
But smoke also contains 100s of gases
Notes: 1. WHY SMOKE RESEARCH IS IMPORTANT

## Slide 5
Transport
Chemical & physical transformations
Surface deposition
ATMOSPHERIC MODELS
EMISSIONS MODELS
From Fire to Smoke Impacts
IMPACTS
COMPOSITION
Bruce Sounder/Flickr CC
PM2.5
C6H6
CH2O
CH3OH
C10H16
NO2
NO
HCN
NH3
C3H4O
Notes: 3. COMPOSITION -> EMISSIONS -> TRANSPORT -> IMPACTS (TIE’EM ALL TOGETHER). Image SEA from High Country News (hcn.org, https://www.hcn.org/issues/50.17/latest-wildfire-smoke-deaths-could-double-by-centurys-end original source Bruce Sounder/Flickr CC). Seely Lake Aug 22, 2017 (MT DEQ)

## Slide 6
Composition – Relative abundance of pollutants in smoke
How does composition vary with fire behavior, fuel properties, and environmental conditions?
Where, when, & how much of various pollutants are produced?
Monitoring – Impacts of smoke on ambient air quality
Smoke Research at the Missoula Fire Sciences Laboratory
Emissions – Amounts of pollutants (smoke) produced
Where does the smoke go? What are impacts on atmospheric composition?
Transport – Atmospheric transport of smoke local to regional scales
Notes: 2. WHAT SMOKE RESEARCH IS AT THE FIRE LAB

## Slide 7: Emissions
Emission of air pollutant X (mass/area/time) estimated as:
emission
factor
×
Emissions of X
fuel
loading
×
combustion
completeness
×
area
burned
=
Mapped fuel
classification system
Satellite remote sensing:
burn scars
active fire detections
Infrared flight fire perimeter
Fuel consumption model
Satellite remote sensing:
fire energetics
burn severity
EFX
field & laboratory studies
Where, when, & how much of various pollutants are produced?
Emissions

## Slide 8
Smoke Composition – What’s in the Smoke
Understand how the interaction of fuel properties, fire behavior, and environmental conditions control smoke composition
Fresh smoke contains 100’s of pollutants
Composition is quantified with
Emission Factors (EF)
EFX vary considerably
Notes: 4. SMOKE COMPOSITION: WHAT’S IN SMOKE & HOW/WHY COMPOSITION VARIES

## Slide 9
Smoke Composition – Laboratory and Field Studies

## Slide 10: Measurement of Emission Factors - Carbon Mass Balance Method
All the volatilized carbon species are measured
Emissions are well mixed
well mixed
smoke plume
background
air
background
air
smoke sample
Emission of species i is:
Sum of volatilized carbon
Fuel carbon fraction
Smoke Composition – Measuring Emission Factors (EF)
Smoke includes
100’s of VOC
Nitrogen compounds
PM diverse in size & composition
Relative abundances vary
Fuel properties
Fire behavior
Environmental conditions
Notes: This slide illustrates the different combustion processes. Describe the difference between pre-ignition, flaming, and smoldering processes.

## Slide 11
COMPOSITION
ATMOSPHERIC
MODELS
Plume Rise
H
H
Transport
Chemistry
Removal
Bruce Sounder/Flickr CC
Emission Factors: Just one piece needed for smoke impacts
IMPACTS

## Slide 12
THANK YOU !
Invitation
Tour of Missoula Fire Sciences Laboratory
September 8, 2022
QUESTIONS?
USFS – EPA
Smoke Monitor Evaluation
Combustion
Lab
New
Combustion
Facility
Wind Tunnel

## Slide 13: PM2.5 Emission Factors
Smoke production models assume fixed flaming-to-smoldering ratios for litter fuels
Hypotheses Smoldering and EFPM2.5 increase with:
Increasing conifer litter bulk density (BD)
Burn Ponderosa Pine needle fuelbeds in laboratory and measure emissions for varied bulk density
Measure modified combustion efficiency (MCE) to quantify smoldering combustion and EFPM2.5
FOFEM and CONSUME: Models for planning prescribed burns and managing smoke impacts

## Slide 14: PM2.5 Emission Factors
Smoke production models assume fixed flaming-to-smoldering ratios for litter fuels
Hypotheses Smoldering and EFPM2.5 increase with conifer litter bulk density (BD)
Test Burn Ponderosa Pine needle fuelbeds in laboratory and measure emissions for varied bulk density
FOFEM and CONSUME: Models for planning prescribed burns and managing smoke impacts
Bulk density – 4 groups:
Very low, 13 kg m-3
Low, 25 kg m-3
Moderate, 51 kg m-3
High, 76 kg m-3
Fir / Spruce
25
85
Loblolly Pine
Jack / Red Pine
Ponderosa Pine
50
Bulk density, BD
(kg m-3)

## Slide 15: PM2.5 Emission Factors
Burn Ponderosa Pine fuelbeds (fixed dimensions)
Measure emissions: MCE and EF for CO2, CO, PM2.5, CH4
Cavity ring-down spectroscopy
PM2.5 filter samples
Fuelbed
12 in x 12 in x 1 in
Missoula Combustion
Facility

## Slide 16: PM2.5 Emission Factors
EFPM2.5 increases with fuelbed litter bulk density
PM2.5 emissions likely underestimated for prescribed fires with significant needle litter component
Current smoke management tools predict less pollutant emissions
Results
Implications

## Slide 17: Fuel Classification System
Assign fuel class to map pixels
Estimate loading of
fuel components
Keane, Robert E. 2015. Wildland fuel fundamentals and applications. Springer. 191 p.
Urbanski, S. et al. 2018. Contiguous United States wildland fire emission estimates during 2003-2015. Earth System Science Data. 10: 2241-2274.

## Slide 18
Missoula Fire Lab Emission Inventory (MFLEI)
Retrospective wildland fire emission inventory for CONUS
designed to
Quantify impacts of wildfires on air quality and public health in the US at local, regional, and national scales
Evaluate & improve smoke forecasting techniques
Support the development of effective and efficient emission control strategies
Better understand consequences of fire/land management, individual decisions and overall policy on air resources

## Slide 19
MFLEI advantages over real-time and retrospective global fire emission inventories
Detailed fuels available only for CONUS
Post-fire burned area & burn severity from satellite borne sensors and fire management perimeters from airborne IR imagery
Fuel consumption models developed for fires in CONUS ecosystems
Emission factors measured for fires in CONUS ecosystems
Missoula Fire Lab Emission Inventory (MFLEI)
Provides daily burned area, fuel consumption, and pollutant emissions at a 500 m x 500 m resolution

## Slide 20
Fuel classification system:
Fuel classification system map:
Fuel consumption:
Pollutant Emission Factors:
Synthesis of published field and laboratory studies
Fire burned area & date:
Multiple data sources
Forest Fuel Type Groups
USDA Forest Service Forest Type Group Map
First Order Fire Effects Model (FOFEM) for litter and duff
CONSUME for down dead wood, herb, and shrub
Miller and Yool (2002) for forest canopy
Missoula Fire Lab Emission Inventory (MFLEI)

## Slide 21
emission factor
(EFX)
×
EmissionX
fuel
loading
×
combustion
completeness
×
area
burned
=
Mapped fuel
classification system
Airborne IR fire perimeters
Satellite remote sensing
  Burned area
  Burn severity
  Active fire detections
Published field & lab measurements
Parsons et al. (2010) RMRS-GTR-243
Fuel consumption models
(FOFEM and CONSUME)
EFX – EF for emissions of species X (CO, PM2.5, CH4,….)
Missoula Fire Lab Emission Inventory (MFLEI)
Forest fuels based on >29,000 USFS Forest Inventory & Analysis Program plots

## Slide 22
Annual PM2.5 emitted by wildfires in western US
PM2.5 emitted (Gg y-1)
Anthropogenic emissions
2014 EPA NEI
2% of wildfire days account for  50% of emissions
On these days:
Wildfires: major source of PM pollution in western U.S.
PM2.5 Emitted (Gg/y)
Daily wildfire PM2.5 emitted
2003-2015
Wildfire
PM2.5
≥ 10 x
Anthropogenic
PM2.5
Urbanski et al. (2018)

## Slide 23
Quantifying impacts of wildfires on urban air quality
MFLEI emissions
Atmospheric transport model
Salt Lake City 2007 Wildfire Season
Wildfire contributions towards air pollution (CO) at Salt Lake City
Idaho
52%
CA & NV
28%
Utah
15%
Mallia, D. V., J. C. Lin, S. Urbanski, J. Ehleringer, and T. Nehrkorn (2015),
Impacts of upwind wildfire emissions on CO, CO2, and PM2.5 concentrations in Salt Lake City, Utah, J. Geophys. Res.Atmos., 120, 147–166, doi:10.1002/2014JD022472

## Slide 24
Large discrepancies exist between emission inventories
MFLEI: Missoula Fire Lab Emission Inventory
FiNN: Fire INventory from NCAR
GFED: Global Fire Emission Database
WFEIS: Wildland Fire Emissions Information System
Rigorous evaluation of inventories is needed across time & spatial scales relevant to air quality impacts.
t: 1 – 30 days
x: fire event, air shed, regional